## Slide 1: final Presentation
G5

## Slide 2: Recap:Baseline

## Slide 3: Recap:Baseline
Area：238238 um^2
Cycle time：10 ns
Cycle (no hazard)：1915 ns
Cycle (has hazard)：24245 ns

## Slide 4: Our Goal
ID stage forwarding
Reduce redundant x0 write operation
Cache
Extension
  Compression
  BP
Qsort

## Slide 5: ID stage forwarding
If the data used for judging jump or branch situation had already completed, forwarding it from MEM stage to ID stage. Otherwise, add a bubble.

## Slide 6: Our Goal
ID stage forwarding
Reduce redundant x0 write operation
Cache
Extension
  Compression
  BP
Qsort

## Slide 7: Reduce redundant x0 write operation
If an instruction writing data to x0, then turn signal RegWrite to 0.

## Slide 8: Our Goal
ID stage forwarding
Reduce redundant x0 write operation
Cache
Extension
  Compression
  BP
Qsort

## Slide 9: Cache Optimization
Read-only I-cache
To solve setup time error
  Register mem_ready
  Save the data into register at the next cycle
If miss&dirty, first read data from memory, then write dirty block back to memory

## Slide 10: Cache Optimization
Reduce more cycles
miss
&
dirty
miss
&
dirty
write
back
write
back
read
data
read
data
Processor stall
Processor stall
Before
After
Processor can run while write back

## Slide 11: Our Goal
ID stage forwarding
Reduce redundant x0 write operation
Cache
Extension
  Compression
  BP
Qsort

## Slide 12: Compression
Need two cycle to fetch cross block data (I5)
Use a 16-bits buffer to store previous instruction

## Slide 13: Compression

## Slide 14: Compression
Need two cycles to fetch cross block data
Sol：
  Read 48-bits at a time
  Change cache block size to 16-bits

## Slide 15: Compression Testbenches
sdc_cycle = 4.0
tb_cycle = 4.0
Always not taken
 | Timing (ns) | Area (um^2) | AT
Decompress | 2494 | 240870 | 600729780
Compress | 2114 | 253210 | 544887728

## Slide 16: Our Goal
ID stage forwarding
Reduce redundant x0 write operation
Cache
Extension
  Compression
  BP
Qsort

## Slide 17: Branch Prediction
2-bit predictor
2-level 1-bit saturation predictor

## Slide 18: 2-level 1-bit saturation predictor(n=2)
Remembers the history of the last 2 occurrences
Works efficiently on regularly recurring pattern
Ex : a conditional jump is taken every third time
0->1
0
0
0
Branch sequence:001001…
00
1
0
0
0
1
0
0
0
01
10
Branch history
Branch history
Branch history

## Slide 19
a=10, b=20, c=30
Cycle time = 10.0 ns
Branch Prediction | Timing (ns) | Area (um^2) | AT
Always not taken | 4565 | X | X
2-bit predictor | 4495 | 228449 | 1.03*10^9
2-level 1-bit saturation predictor | 4155 | 229795 | 0.95*10^9
Branch Prediction Testbenches

## Slide 20: Our Goal
ID stage forwarding
Reduce redundant x0 write operation
Cache
Extension
  Compression
  BP
Qsort

## Slide 21: QSort Testbench - Compression
sdc_cycle = 4.0
Always not taken
 | Tb_cycle | Timing (ns) | Area (um^2) | AT
Decompress | 4.0 | 673446 | 240870 | 1.62e11
Compress | 4.2 | 624378 | 253210 | 1.58e11

## Slide 22
sdc_cycle = 4.0
tb_cycle = 4.6
Total 8327 branch instructions
Branch Prediction | Prediction wrong | Error rate | Timing (ns) | Area (um^2) | AT
2-level 1-bit saturation predictor | 4778 | 57.38% | 667738 | 270044 | 1.80e11
2-bit predictor | 4610 | 55.36% | 667434 | 267729 | 1.786e11
QSort Testbench – Branch Prediction

## Slide 23
sdc_cycle = 4.0
tb_cycle = 4.6
Total 8327 branch instructions
Branch Prediction | Prediction wrong | Error rate | Timing (ns) | Area
2-bit predictor | 4610 | 55.36% | 667434 | bigger
Always not taken | 4885 | 58.66% | 667351 | smaller
QSort Testbench – Branch Prediction

## Slide 24
Compression
Always not taken
Sdc cycle(ns) | Tb cycle(ns) | Timing (ns) | Area (um^2) | AT
2.9 | 3.3 | 493717.95 | 296454 | 1.46*10^11
3.0 | 3.2 | 489508.8 | 285771 | 1.40*10^11
3.1 | 3.5 | 511880.25 | 289519 | 1.48*10^11
3.3 | 3.5 | 511880.25 | 277657 | 1.42*10^11
3.5 | 4.0 | 571574 | 265411 | 1.52*10^11
3.7 | 4.0 | 5717574 | 261532 | 1.49*10^11
3.9 | 4.4 | 613956.2 | 255710 | 1.57*10^11
QSort Testbench

## Slide 25: Work Assignment Chart
劉心宇 | ID stage forwarding & Compression
廖苡鈞 | Branch predictor & Cache
陳俊霖 | Branch predictor & ppt